## Slide 1
ROI Privacy-Preserving
Edge Streaming
A Resilient Surveillance System for Unreliable Networks
ICT Application Technology — Final Project
Jungha [name] Spring 2026
PRIVACY · REAL-TIME · RESILIENT

## Slide 2
The Surveillance Paradox
THE PROBLEM
Full video transmission raises
privacy concerns
Networks are unreliable:
packets drop, latency spikes
Bandwidth constraints in
distributed surveillance
OUR SOLUTION
Transmit only ROI (people)
— background discarded at edge
Real-time recovery
from packet loss
Adaptive quality control
via closed-loop PID
➜

## Slide 3
System Architecture
Two Logically Separated Nodes
EDGE Jetson Orin Nano
Camera / Video source
YOLOv8n (TensorRT) — detect
Patch Extractor (JPEG encode)
UDP Sender + Header Redundancy
Feedback Receiver
SERVER Laptop
Packet Receiver + Reorder Buffer
Recovery: ZoH + Kalman + Predict
Stitcher (frame reassembly)
Decision Machine + PID
Live View + Security State
UDP CHANNEL
Simulated Drop + Delay
patches ▶
◀ feedback
Privacy: background discarded at edge — never transmitted
Adaptive: closed-loop quality control via PID feedback

## Slide 4
Four Layers of Recovery
01
Frame Header Redundancy
Each frame header sent 5×.
At 50% packet drop, total-loss
probability = 3%. Frames almost
never lost.
02
Zero-order Hold Recovery
When a patch fails to arrive,
reuse the previous frame's patch
image. The person doesn't
disappear.
03
Kalman Compensation
Estimates each person's velocity
and translates the recovered
patch to the predicted position.
Eliminates misalignment.
04
Predict-only Mode
When detection itself fails,
Kalman generates virtual patches
at expected positions. Tracking
continues.
Adaptive Control Loop
PID Controller adjusts JPEG quality (30–95) from reception ratio 3-State Machine Normal / Warning / Emergency

## Slide 5
Live Demo
Real-time system response to network degradation

## Slide 6
ROI Privacy-Preserving Edge Streaming
Privacy by Design
Only ROI patches transmitted — background discarded at the edge
Adaptive by Necessity
PID controller closes the loop on JPEG quality from reception ratio
Resilient by Engineering
Four layers of recovery: from frame headers to predict-only mode
Thank you.
github.com/jungha · ICT Application Technology, Spring 2026